## Slide 1: POL Next Generation LAN Networks Anovidan Investments Ltd
Introduction to Passive Optical LAN
Changing the Landscape of Enterprise Infrastructure

## Slide 2
POL – ECO friendly solution
Single Mode Fiber
Voice, Data, Video & Other
Serves 128 with PON
Capacity measured in Tbps
CAT5e
Data only
Serving 120 end-points
Capacity in Mbps
CAT3
Voice only
Serving 120 end-points
Capacity in Kbps
POL Next Generation LAN Networks
Anovidan Investments Ltd

## Slide 3: Basic Premise of POL
IDF
Office Space
MDF
Floor n
Access
Switches
WLAN
Short
CAT-5/6
Core
Router
Distribution
Switch
Copper-based Ethernet LAN
56
PON
Ports
4-port
Optical Line
Terminals
Fiber 8
Fiber 1
PON 1
PON x
Optical Line
Terminal
WAN
Floor 1
Access
Switches
Short
CAT-5/6
Passive Optical LAN
Long
CAT-5/6
Long
CAT-5/6
Fiber 32
Fiber 1
WLAN
7000+
Ethernet
Ports
Served
4
8
1700+
ONTs
Fire Suppression
32
Heavy Duty Cable Trays
Heavy Duty Cable Trays
UPS
AC
HVAC
Multi-Mode Fiber
Single-Mode
Fiber
(20km reach)
Light weight or no Cable Trays
Light weight or no Cable Trays
Long PoE
Cables
Long PoE
Cables
Short PoE
Cables
Short PoE
Cables
8
8
8
POL Next Generation LAN Networks
Anovidan Investments Ltd

## Slide 4
Less Energy, Less Space, More Scalable
18 Racks
90% space reduction
Traditional LAN (2.000 users)
POL (8.000 users)
1 Rack
4x the number of users!
POL Next Generation LAN Networks
Anovidan Investments Ltd

## Slide 5
POL – GPON in Building Architecture
POL Next Generation LAN Networks
Anovidan Investments Ltd

## Slide 6
GPON Passive Optical Network (PON)
Optical Splitter
(1:32 or 1:16)
Optical Network Terminals (ONT)
Optical Line Terminal (OLT)
1490nm
1310nm
1G or 10G
Network
Uplinks
20km/12mi to 30km/18mi
Single mode fiber
Single mode fiber
Passive Optical Network (PON)
Completely passive infrastructure
Single fiber carries multiple wavelengths
2.48 Gbps downstream
1.24 Gbps upstream
Serve Remote Buildings Up to 20Km to 30Km
POL Next Generation LAN Networks
Anovidan Investments Ltd

## Slide 7: GPON
Each PON supports a single optical fiber carrying 2 wavelengths, a rate of 2.4G/1.2G, up to 64 end devices, and a maximum span of 20km
GPON Standard Supports Overlay Wavelengths within the 15xx range
  Currently used to support RF-based video delivery
  In the near future will be used to support DWDM services
Data
Switched Video
Voice
0 – 20Km
  1310 nm upstream (TDMA) carrying Voice, Data and Video Signaling traffic
  1490 nm downstream (TDM) carrying Voice, Data and Switched Video traffic
1:32
Desktop
Terminal
(ONT)
MTU
Terminal
(ONT)
1310 nm
1490 nm
Analog &
QAM Video
1550 nm
OLT: Optical Line Terminal
POL Next Generation LAN Networks
Anovidan Investments Ltd

## Slide 8: Next Generation of Enterprise LAN
Passive
Network
Zhone MXK
OLT
Zhone zNID
ONT
Present Method of Deployment
Layers of Routers & Switches
Zhone FiberLAN
zPON
Splitter
Zhone Confidential
Campus Aggregation
Building Aggregation
Communication Closet
End User

## Slide 9: Footprint Savings
75 Users
250+ Users

## Slide 10: Association for Passive Optical LAN
NEW YORK – August 6, 2013 – Corning, IBM, SAIC, TE Connectivity, Tellabs,
Zhone and 3M have formed the Association for Passive Optical LAN (APOLAN).
The association’s mission is advocating for the education and global adoption
of passive optical networks in the local area network (LAN) industry.
POL Next Generation LAN Networks
Anovidan Investments Ltd

## Slide 11
Single-mode fiber used to support advances future generations of PON technology:
  LAN network can be upgraded without new cable infrastructure deployment.
  Scalable infrastructure can support over 100Tbps bandwidth.
Optical LAN Solution Lifespan
Traditional Ethernet Solution Lifespan
5-8 YEARS
30 YEARS
POL –Scalable & Future Proof
POL Next Generation LAN Networks
Anovidan Investments Ltd

## Slide 12
ONT Zone Application
ONT under-desk mount version
ONT wall-mount version
Appliance outlet
SECURE Wall Box version
ONT Installation
POL Next Generation LAN Networks
Anovidan Investments Ltd

## Slide 13: Passive Optical LAN Building Service Integration
VoIP
Phone
WiFi
Access Point
Surveillance
Camera
Video
Conferencing
Building
Automation
Systems
Desktop
Computer
PON
Splitter
RF Video
IP Video
IP / Ethernet
Data
Packet Voice
Analog Voice
POL Next Generation LAN Networks
Anovidan Investments Ltd

## Slide 14
Redundancy
June 8, 2015
Tellabs Confidential Proprietary
14
  A 2:x PON splitter provides both protection, redundancy and splitting functions
  Supported across different PON cards in same OLT or between different OLTs in geographically dispersed locations
  A means to provide fiber route diversity between OLT and 2:x ODN splitters
  Supported for 2:8, 2:16, 2:32 ODN splitters
2:32
Splitter
Block Diagram
2 x N Splitter
Type B PON redundancy
via 2:x ODN splitter
POL Next Generation LAN Networks
Anovidan Investments Ltd

## Slide 15
Tellabs® Panorama OLAN Manager Faster Moves, Adds and Changes!
June 8, 2015
Tellabs Confidential Proprietary
15
Centrally accessed element management provides efficiencies over CUI accessed at every OLT, VGW and ONTs
Panorama OLAN Manager key features
  Topology Manager ~ Offers a complete view of entire LAN and campus wide network
  Events/Alarm List Manager ~ Streamlines events/alarms monitoring and resolution
  Service Provisioning ~ Global profiles speed service provisioning and moves/adds/changes
  Security Manager ~ Role-based access, security privileges, activity logging which leads to better employee training and less rogue events
  Report Manager ~ Customized and automated report generation
  Scheduler for Automatic Backups ~ Scheduled and on-demand back-up and restoration of network configuration databases
  Online Help Utility ~ Hot-linked documentation for operational efficiency and better employee training
POL Next Generation LAN Networks
Anovidan Investments Ltd

## Slide 16: Space Requirements
From This
To That
Up to 90% Less space
No Need for floor closets

## Slide 17: Security & Privacy
From This
To That
Cannot be tapped - No magnetic field Encrypted

## Slide 18: Maximum Distance
To That
20km
From This
100 meters

## Slide 19
Stable
June 8, 2015
19
Improve LAN reliability and operational efficiencies
Carrier-class 99.999%/Five 9s availability = 5 minutes downtime per year
  One OLT, one SMF, one ODN splitter and one ONT achieves five 9s
  Equipment redundancy
    Common control, Ethernet switch units, network connectivity, power & fans
  On average, a business loses $5,600 per minute in an LAN outage
Network redundancy
  Dual homing to core routers
  Type-B PON redundancy
    PON ODN redundancy with geographically dispersed OLTs
    Fiber route diversity
    Achieve 99.9999%/six 9s availability with only 30 seconds network downtime annually
Graceful migration of future technology, fewer “rip and replace” events
  Analog voice  IP voice, and RF video  IP video, can be accommodated
  Single mode fiber infrastructure best future-proof choice today
  2.4GbE OLT/ONTs can migrate to 10GbE GPON per end-point
POL Next Generation LAN Networks
Anovidan Investments Ltd

## Slide 20
Reliability - MTBF
POL Next Generation LAN Networks
Anovidan Investments Ltd

## Slide 21
Availability and Resiliency
Availability and Resiliency
  OLTs have redundant power, cooling, logic/switching cards and backplanes
  OLT/ONT typically 5-9s (99.999%) available (5.25 minutes down time annually)
Source: Cisco Enterprise Campus 3.0 Architecture: Overview and Framework
This architecture requires the use of two fiber NIC cards in each end user workstation
OLAN Reliability = > 99.999% (5.25 downtime Minutes/Year)
Reliability = > 99.938% (325 downtime Minutes/Year)
Reliability = > 99.961% (204 downtime Minutes/Year)
Reliability = > 99.9999% (30 downtime Seconds/Year)
~ 5.4 hours
~ 3.5 hours
5-9s/5mins with less equipment and 6-9s/30seconds using Type-B PON redundancy!
Legacy
Copper
Based
LAN
POL Next Generation LAN Networks
Anovidan Investments Ltd

## Slide 22
FiberLAN Access Concentrator Chassis MXK 823, 819, 319, 198, 194
Scalability
High Bandwidth
Intelligence
High Reliability
Efficiency
Security
Performance
Notes: Scalability, Bandwith, Intelligence, Reliability, Efficiency, Security, Performance => MXK

## Slide 23: Indoor ONTs – 2300 Series
2301 ONT:
CE certification
-EU and -UK models available
Models Available | Description
ZNID-GPON-2301-00 (planned) | GPON Uplink, 1 GE with no Power Supply
ZNID-GPON-2301-EU | GPON Uplink, 1 GE with EU Power Supply
ZNID-GPON-2301-UK | GPON Uplink, 1 GE with UK Power Supply

## Slide 24: Indoor ONTs – 2400A Series
Model Group | Uplink Type |  |  |  | Ports |  |  | 
 | GPON | 1G Fiber | 100M Fiber | 10/100/1000 Copper | POTS | GigE | WiFi | RFV
2402A | -GPON | -GE |  |  |  | 2 |  | 
2403A | -GPON |  |  |  |  | 2 |  | Yes
2424A | -GPON | -GE | -FE | -CU | 2 | 4 |  | 
2425A | -GPON |  |  |  | 2 | 4 |  | Yes
2426A | -GPON | -GE | -FE | -CU | 2 | 4 | Int | 
2427A | -GPON |  |  |  | 2 | 4 | Int | Yes
2426A-EUR | -GPON |  |  |  | 2 | 4 | Rem | 
2427A-EUR | -GPON |  |  |  | 2 | 4 | Rem | Yes

## Slide 25: Indoor ONTs – 2600 Series
Model | Description | Model | Description
ZNID-GPON-2608T | GPON Uplink, 0 POTS, 8 GE with PoE | ZNID-GE-2608T | 20 km GE Uplink, 0 POTS, 8 GE with PoE
ZNID-GPON-2624A | GPON Uplink, 2 POTS, 4 GE | ZNID-GE-2624A | 20 km GE Uplink, 2 POTS, 4 GE
ZNID-GPON-2624P | GPON Uplink, 2 POTS, 4 GE (PoE) | ZNID-GE-2624P | 20 km GE Uplink, 2 POTS, 4 GE (PoE)
ZNID-GPON-2628A | GPON Uplink, 2 POTS, 8 GE | ZNID-GE-2628A | 20 km GE Uplink, 2 POTS, 8 GE
ZNID-GPON-2628P | GPON Uplink, 2 POTS, 8 GE (4 with PoE) | ZNID-GE-2628P | 20 km GE Uplink, 2 POTS, 8 GE (4 with PoE)
ZNID-GPON-2628T | GPON Uplink, 2 POTS, 8 GE with PoE | ZNID-GE-2628T | 20 km GE Uplink, 2 POTS, 8 GE with PoE
ZNID-GPON-2644A | GPON Uplink, 4 POTS, 4 GE | ZNID-GE-2644A | 20 km GE Uplink, 4 POTS, 4 GE
ZNID-GPON-2644P | GPON Uplink, 4 POTS, 4 GE (PoE) | ZNID-GE-2644P | 20 km GE Uplink, 4 POTS, 4 GE (PoE)
ZNID-GPON-2648A | GPON Uplink, 4 POTS, 8 GE | ZNID-GE-2648A | 20 km GE Uplink, 4 POTS, 8 GE
ZNID-GPON-2648P | GPON Uplink, 4 POTS, 8 GE (4 with PoE) | ZNID-GE-2648P | 20 km GE Uplink, 4 POTS, 8 GE (4 with PoE)
ZNID-GPON-2648T | GPON Uplink, 4 POTS, 8 GE with PoE | ZNID-GE-2648T | 20 km GE Uplink, 4 POTS, 8 GE with PoE
Model Tip: 26XXA = no PoE; 26XXP = 4 PoE; 26XXT = 8 PoE
2600A/P/T

## Slide 26: zNID 2800 Series FiberJACK ONT’s
FiberJACK 2800 Series (Wall-Plate ONT)
2804P Models
  GE and GPON (SFF) Optics
  4 GE LAN ports
  Full RG functionality (3.0.x SW)
  LLDP-MED, 802.1X on Secure Access models
  LED Normal/Min/Dark modes
  Cover-Off detection switch & alarm
AC version
  Mounts in standard outlet box in wall
  100-240 VAC 50/60 Hz (3-wire pigtail)
  PoE (20W total power available for delivery)
DC version
  Outlet box NOT required (Low Voltage / Open Frame)
  Dual inputs: 2-wire direct power feed – OR – CAT5 PoE IN
  PoE (30W total power available for delivery)
Office/Enterprise/Government markets

## Slide 27: Passive Optical LAN Market Adoption
Federal Government DoD / Civilian
Dept Energy Sandia National Lab
Dept Homeland Scty “St Elizabeth’s”
Health & Human Services
Intelligence Agencies
NASA Stennis Space Center
State Department, US AID
US Air Force Andrews AFB
US Air Guard Andrews AFB
US Army Honduras, FT Huachuca
US Army Reserves South East
USDA Forest Service
US Marine Corps
Camp Pendleton Hospital
MCB Quantico
MCB 29 Palms
Okinawa, Japan
MCD Albany, GA (pending)
Others (unannounced)
Commercial
TIA Headquarters
Deltek Corporation
San Diego Public Library
Schriever Air Force Base (housing)
Buccamment Bay Resort
Others (unannounced)
  Hotels, University
  Healthcare facilities
  Financial firms
Sandia National Labs
Dept of Homeland Security
St. Elizabeth’s campus
TIA Headquarters
San Diego
Public Library
POL Next Generation LAN Networks
Anovidan Investments Ltd

## Slide 28: 2010 Department of Army Directive Technical Guidance for Network Modernization April 23, 2010
POL Next Generation LAN Networks
Anovidan Investments Ltd

## Slide 29
TCO – Case Review
Sandia National Laboratory
Sandia National Laboratory before Optical LAN
  13,000 users, 265 buildings & 600 active switches
  First cost installation around $3K to $5K per port
  Each switch in 3’Wx3’Dx7’H racks (600 total racks)
  Individual management across 265 buildings
After Tellabs Optical LAN
  14 active Optical LAN switches
    98% reduction
  Optical LAN OLT is the size of a microwave
    90% reduction in size
  Optical LAN will reduce total energy consumption by 65%
    Saves 1 million kilowatt hours per year
  First cost installation approximately $1.5K to $2K per port
    60% reduction in equipment and installation costs
  Centralized management of all users, buildings & Optical LAN equipment
Sandia National Laboratory
Sandia calculates $20M will be saved over 5 years compared to legacy copper based LAN!
POL Next Generation LAN Networks
Anovidan Investments Ltd

## Slide 30
POL – Key Value
Summary
POL Next Generation LAN Networks
Anovidan Investments Ltd

## Slide 31
Hospitals
Campuses
Universities
Cruise Ships
Hospitality
Government and Military
High Occupancy Buildings (Call Centers)
Multi-Tenant Units (Commercial and Residential)
POL – Target Users
POL Next Generation LAN Networks
Anovidan Investments Ltd

## Slide 32
TCO – Case Review
University of Mary Washington
POL Next Generation LAN Networks
Anovidan Investments Ltd

## Slide 33
Before
After
POL – Eliminates Cable Congestion
POL Next Generation LAN Networks
Anovidan Investments Ltd

## Slide 34
TCO – Case Study
Russell Investments (8 floors)
POL Next Generation LAN Networks
Anovidan Investments Ltd

## Slide 35
Traditional LAN
Core.
Layer 3
Distribution:
Layer2/3
Access:
Layer 2
Edge
End user
workstations
High Cost
High Power Consumption
High BTU Output
Requires HVAC
Large Rack-Space
Footprint
High Cost
High Power Consumption
High BTU Output
Requires HVAC
Large Rack-Space
Footprint
Multiple Cables
High-Cost,
Large-Bundle Cabling
POL Next Generation LAN Networks
Anovidan Investments Ltd

## Slide 36
Passive Optical LAN
Core.
Layer 3
Distribution:
Layer2/3
Access:
Layer 2
Edge
End user
workstations
Centrally Managed
Better Cradle-to-Grave
“Five Nines” Reliability
Reduced Thermals
Reduced Rack-Space
Footprint
Low Cost
Zero Electronics
Zero Power Required
Zero HVAC Required
Zero Rack-Space
Low-Cost Small-
Bundle Cabling
PoE Enabled
Same Services &
Applications
as Active Ethernet
1x32 Passive
Splitter
POL Next Generation LAN Networks
Anovidan Investments Ltd

## Slide 37
POL – Total Cost of Ownership (TCO)
POL Next Generation LAN Networks
Anovidan Investments Ltd

## Slide 38: Zhone FiberLAN A Green Technology Solution

## Slide 39: Summary
FiberLAN Enables “Green-deployment” reduction in enterprise wide power and space consumption
FiberLAN provides Increased “Life-expectancy” of fiber based infrastructure 25 years vs. 10-15 years for copper
FiberLAN Reduces Management cost due to ease of use with Zhone EZ Touch and ZMS Network Management.
FiberLAN Reduces installation cost based on individual Fiber optic cable run supporting up to 64 ports or splits per PON (POL) port.
FiberLAN is highly secure
FiberLAN delivers “Unlimited Bandwidth” potential (GPON) today, upgrade to “wire speed” Active Ethernet if required in the future.

## Slide 40
Brief History of POL
POL Next Generation LAN Networks
Anovidan Investments Ltd